## Slide 1: ASTR 535
Observational Techniques
Fall 2023
Observing principles and tools

## Slide 2: Topics 9/12
Questions
Exposure time calculator
New module : observing concepts and tools
  APO observing trip schedule : Fri-Sun 10/20B, 10/21B, 10/22A
    4th quarter NMSU programs
  Time systems
  Coordinate systems
  Observability

## Slide 3: Coordinate systems and time
Time
  Solar and sidereal time
Coordinates
  right ascension / declination
  hour angle / declination
  az / alt
  airmass

## Slide 4: What time is it?
Local legal time?
Universal time (UT)?
Sidereal time?
If you were observing right now, what would be the optimal right ascension?

## Slide 5: Observability
What do you need to know to determine if/when an object will be observable?
How long will it be observable?
HA = LST – RA
How high will it get?
  at HA=0, zenith distance = |Dec – latitude}
Airmass : how is airmass related to zenith distance?
X ~ sec(Z)

## Slide 6: Observability tools
From John Thorstensen, Dartmouth:
  skycalendar / skycalc : C programs, text output
  JSkyCalc : Java, graphical output
    Installation and demo : seasonal observability, nightly almanac, hourly circumstances, airmass graphs, object lists
astroplan : astropy-affiliated package
  Various tools, graphical output
  Note: interface implemented in pyvista
Airmass.org

## Slide 7: Observability
See Canvas assignment

## Slide 8: Topics 9/14
Questions
Summing and averaging measurements
Observation planning
TMO observing : Mon/Tues/Wed evenings next week?
Exposure time calculator
Telescope use and planning
Digital images and image display

## Slide 9: Summing and averaging
Weighted averaging of different measurements
Expected scatter vs observed scatter

## Slide 10: Observation planning
Sidereal time and right ascension
  (mean) Sun is always on the meridian at noon (modulo daylight savings)
  Sidereal clock runs just a tiny bit faster than solar clock, so in a given day, one hour of solar time is almost the same as one hour of sidereal time
  On vernal equinox, Sun is at RA=0hr, by definition. So 0hr crosses meridian at noon, hence 1h crosses at 13:00, 2h at 14:00, …. 12h at midnight
  The 4 minutes per day difference between sidereal and solar adds up: after 15 days it amounts to 1 hour, after 30 days, 2 hrs, etc.
  So each month after the vernal equinox, the RA of the Sun increases by 2 hours: so on April 21, Sun is at RA=2h (and 14h crosses meridian at midnight),on May 21, Sun is at RA=4h (and 16h crosses meridian at midnight), etc. etc….

## Slide 11: Image display
See Canvas assignment

## Slide 12: 9/18 (Monday night)
TMO demo/training

## Slide 13: 9/21
Questions
Next week
TMO observing
Working with digital images
  File formats
  Calculating expected noise
  Basic data reduction
TMO data inspection

## Slide 14: TMO observing planning
The initial TMO observing project will be:
Determine the instrumental zeropoints for TMO for the 5 Sloan filters (SU, SG, SR, SI, SZ)
Estimate the combined throughput of telescope, optics, and detector for each filter

## Slide 15: TMO project observing resources
For photometric zeropoints, want stars with known magnitudes
  If we wanted to get more subtle, would include stars with a range of colors to see if there are color-dependent zeropoints, i.e. transformation terms
Traditionally, e.g., UBVRI used fields with relatively bright (V~-10-12) standard stars, e.g. Landolt fields http://articles.adsabs.harvard.edu//full/1992AJ....104..340L/0000340.000.html
  Note Selected Areas
For SDSS, the actual photometric system is defined by the SDSS observations themselves
  These are saturated for bright stars!
  A u’g’r’i’z’ system was set up which is close, but not identical to SDSS. These used the same Landolt fields, Smith et al 2002, see table 7. It will suffice for our use!
  For finding charts, see Landolt paper
    Smaller fields: http://james.as.arizona.edu/~psmith/61inch/ATLAS/tableA.html
  Choose fields based on LST at observation time
  What do you expect for exposure times?
For throughput, want spectrophotometric standard, e.g. from http://www.eso.org/sci/observing/tools/standards/spectra.html

## Slide 16: TMO observing
See astronomy.nmsu.edu/tmo-wiki, esp TMO Users guide HowTo
Get a VNC client to connect to desktop
Alternatively/additionally, go to http://tmo.nmsu.edu for web based control

## Slide 17: TMO observing resources
General observing procedure:
  Connect to TMO desktop by VNC to tmo.nmsu.edu or to web interface (tmo.nmsu.edu)
  Open dome
  Focus
  Slew to star(s)
  Take exposures
  Take calibration frames: darks (match exposure times) and twilight flats
Data will be automatically synced to astronomy.nmsu.edu
  In the morning, link in /home/tmo/YYYYMMDD (also accessible via web http://astronomy.nmsu.edu/tmo/YYYYMMDD (note day number is UT date)
  More quickly, in /home/tmo/Observations/YYYY-MM-DD if taken directly with MaximDL (but note day number is local date)

## Slide 18: TMO analysis
Looking at images
Image analysis
  Image size measurements
  Basic photometry

## Slide 19: pyvista
Demo
  imred module
    Reducer object
    log()
    rd()
  tv module
    TV object
    tv()
    imexam()
  Stars
    mark()
    photom()

## Slide 20: pyvista
Documentation
Installation
  Create conda environment
  pip install astro-pyvista
Running
  ipython –pylab
  Jupyter notebook : %matplotlib qt

## Slide 21: Topics 9/26
TMO status and observing
Exposure time calculator
Next module: effects of the Earth’s atmosphere
Midterm : week of October 10
Looking at TMO data
  Basic image reading, e..g., pyvista imred.Reducer(), rd() and reduce() methods
  Basic image display, e.g.,, pyvista TV tool, tv() method
  Measuring image sizes, e.g. imexam() method of TV tool
  Basic stellar photometry, e.g. stars.mark(), stars.photom()
  Determining gain from flats
  Determining readout noise from biases

## Slide 22: Image inspection
While you may be using pyvista, important to recognize the (relatively simple!) things that are being done
Instantiating a Reducer : sets up parameters for a detector
reduce() : without other arguments, calculates mean overscan level and subtracts it from image. Calculates expected uncertainty in array
TV.imexam() : fits a 2D gaussian to points around cursor
Stars.photom() : simple aperture photometry

## Slide 23: Measuring gain and readout noise
Basic idea: uncertainty (noise) in counts depends on the gain, so measure the noise and determine gain, under the assumption of Poisson statistics (so measure at high level, where readout noise is negligible)
How to measure noise: use flat field, but can’t just look at variation in a region, because there might be real sensitivity variations
  Take the difference between two flats
  Calculate standard deviation in region of ~constant intensity
  G = 2 <C> / 𝜎^2
For readout noise, look at bias frames (C=0) and measure noise in counts in a similar way, convert to noise in electrons using gain

## Slide 24: Exercises
See Image Inspection II in Canvas

## Slide 25: Topic 9/28
TMO Status
Questions
Effects of the Earth’s atmosphere
Atmospheric (and other “background”) emission
Sky model calculator
Exposure time calculator
Image inspection II
  Light transfer curve

## Slide 26
Canvas : sky emission and exposure time calculator
Canvas : image inspection II

## Slide 27: 10/17
Midterm
TMO
APO trip planning
  Logistics: transportation, housing, food
  Introduction to 3.5m
  Science programs
  Observation planning
    Science programs : 1-2 per group
      Concisely summarize the science
      summarize time and conditions (dark/bright) needed
      Summarize location of targets in the sky (first half/second half with more details as needed)
    Proposed observing plans: 10/20B, 10/21B, 10/22A

## Slide 28: 10/19
APO trip planning
  Logistics: transportation, housing, food
  Telescope / instrument / exposure control
  Instrument calibrations
  Observation planning

## Slide 29: TUI and telescope/instrument control in general
Status : where is telescope, what is time, airmass etc
Telescope control
  Slewing
  Offsetting
  Focus
Instrument configuration
  Imagers: filter
  Spectrograph: grating, grating tilt
  Detector: binning, subregion etc
Taking exposures
  File names and locations
  Exposure times
  Start/stop/abort
Acquisition (esp for spectrographs)
  Slit viewer
  Moving object to slit
  Guiding : on slit and offset
Instrument and TUI manuals : https://www.apo.nmsu.edu/arc35m/

## Slide 30: Instrument calibrations
Instrument manauls
ARCTIC
  Flats: dome and twilight
  Biases: (may not be needed, but never hurts to take!)
  Darks?
ARCES
  Internal flats
  Internal wavelength cals : may need to take periodically due to shifts
  Biases (may not be needed, but never hurts to take)
KOSMOS
  External flats and wavelength cals
  Internal flats and wavelength cals
  Biases (as above)
  Flux calibration / standard stars